## Slide 1: High-torque High-precision
https://www.utwente.nl/en/ces/celt/sutq/
Robotic Actuator
Why?
Robotics require actuators with high torque and high precision. This requires high reduction gearboxes. Regular spur gears cause backlash, and the single teeth contact forms a weak spot. Some modern gearbox designs fix this, but they are often expensive. This 3D-printable version is easier to recreate and makes high-end robotics more accessible for everyone.
What?
This is an RV-Reducer, a variation on a cycloidal drive. Cycloidal drives are known for a compact reduction, minimal backlash, and a high shock resistance. All ideal when using softer materials, such as with 3D-printing. The
RV-Reducer adds three shafts and an additional reduction stage. The presented design is optimized for 3D-printing.
The output hub is supported using double bearings.
Cycloidal drives have multiple teeth in contact at once, spreading the load more evenly. One rotation of the eccentric shaft moves the disk over one tooth. This provides a compact reduction. Two disks are used to balance vibrations.
A standard Nema23 stepper motor is used as input. But alternative mounting plates make it easy to use other motors for higher speeds or closed loop control.
Combined reduction of 63:1. Resulting in higher torque and precision at the output.
3D-printed gearbox enabling DIY robotics
The eccentric shaft rotates and causes the cycloidal disk to wobble as needed. Multiple parts lock the bearings in place. It is reinforced with a bolt for higher strength.
Jelmer Volbeda
13-06-2023
The assembly utilizes bolts and threaded inserts for additional reinforcement, resulting in a sturdy and compact gearbox.

## Slide 2: High-torque High-precision
https://www.utwente.nl/en/ces/celt/sutq/
Jelmer Volbeda
13-06-2023
Robotic Actuator
Why?
Robotics require actuators with high torque and high precision. This requires high reduction gearboxes. Regular spur gears introduce backlash, and the single teeth contact forms a weak spot. Some modern gearbox designs fix this, but they are often expensive. This 3D-printable version is easier to recreate and makes high-end robotics more accessible.
What?
This is an RV-Reducer, a variation on a cycloidal drive. Cycloidal drives are known for a compact reduction, minimal backlash, and a high shock resistance. All ideal when using softer materials, such as with 3D-printing. The RV-Reducer adds three shafts and an additional reduction stage. The presented design is optimized for 3D-printing.
On the cycloidal disk multiple teeth contact at once, distributing loads. One rotation of the eccentric shaft cause the disk to move one teeth over. Resulting in a compact reduction. Two disks are used to balance vibrations.
The eccentric shaft rotates and causes the cycloidal disk to wobble as needed. Multiple parts lock the bearings in place. It's reinforced with a bolt for higher strength.
The output hub is supported using double bearings.
A standard Nema23 stepper motor is used as input. But alternative mounting plates make it easy to use other motors for higher speeds or closed loop control.
The frame is held together using bolts and threaded inserts. Those also function as reinforcements.
Combined reduction of 70:1. Meaning: A higher torque and higher precision output.
3D-printed gearbox enabling DIY robotics

## Slide 3: High-torque High-precision
https://www.utwente.nl/en/ces/celt/sutq/
Jelmer Volbeda
Date: 13-06-2023
Robotic Actuator
Why?
Robotics require actuators with high torque and high precision. This requires high reduction gearboxes. Regular spur gears introduce backlash, and the single teeth contact forms a weak spot. Some modern gearbox designs fix this, but they are often expensive. A 3d-printable version is easier to recreate and makes high-end robotics more accessible.
What?
This is an RV-Reducer, a variation on a cycloidal drive. Cycloidal drives are known for a compact reduction, minimal backlash, and a high shock resistance. All ideal when using softer materials, such as with 3d-printing. The RV-reducer adds thee shafts and an additional reduction stage. The presented design is optimized for 3d printing.
On the cycloidal disk multiple teeth contact at once, distributing loads. One rotation of the eccentric shaft cause the disk to move one teeth over. Resulting in a compact reduction. Two disks are used to balance vibrations.
The eccentric shaft rotates and causes the cycloidal disk to wobble as needed. Multiple parts lock the bearings in place. It's reinforced with a bolt for higher strength.
Double bearings support the output.
A standard Nema23 stepper motor is used as input. Alternatively, a BLDC can be used for more speed and to make it back drivable.
Bolts reinforce the frame. And hold everything together using threaded inserts.
Combined reduction of 70:1. Meaning higher torque and higher precision output.
A 3D-printed gearbox enabling DIY robotics.